## Slide 1: Innomotics SG Geared Motors
New IEC Adapter Generation KU
2024

## Slide 2: Innomotics SG Geared Motors New IEC Motor Adapter Generation KU
Rugged, robust and failsafe design with elastic coupling
  Absorption of shock loads & vibrations
  Compensation of slight shaft displacements
Reinforced bearing option available for higher input torques
Sealing option for long service life
FKM sealing option
Bevel gearbox with
IEC motor adapter
Combining the Advantages of K2 and K4 Adapters
Robust
Compact
Very compact dimensions
Length comparable to K4 adapter
Broad motor portfolio accessible
Easy motor assembly and disassembly
Portfolio complexity reduction (universal adapter replaces K4 and K2)
Universal
NEW!

## Slide 3: Innomotics SG Geared Motors New IEC Motor Adapter Generation KU
Compact
Universal
Robust
Size | KU vs. K2 [mm] | KU vs. K4 [mm]
63 | -- | -2
71 | -- | 5
80 | -91 | 4
90 | -91 | 4
100 | -98 | -13
112 | -98 | -13
132 | -139 | 7
160 | -155 | 6
180 | -155 | 6
200 | -165 | 0
225 | -180 | 26
250 | -203 | 6
Elimination of K4/K2 “weak spots”.
Average increase in allowable input torques (T1zul) of >20% with reinforced bearing option.
T1zul
KU adapter is designed for IEC motor flange design B5 – gearboxes with K2/K4 and competitor products easily replaceable.
Combinations of KU adapters with gearboxes – all K2/K4-gearbox combinations available.
MLFB
2KJ3xxx-xxA09-xxxx-Z M2A
Order codes
A30 Reinforced bearing
A35 FKM sealing
A36 Sealing long service life
Adapter sealing options to increase allowable input speed and service life.
Allowable Input Torques
Sealing Options
Optimized Adapter Length
KU is significantly shorter than K2.
Dimensions comparable to K4.
High Compatibility
NEW!

## Slide 4: Innomotics SG Geared Motors New IEC Motor Adapter Generation KU
Features / Function |  | Benefits
One universal solution for all IEC motors. |  | Complexity reduction and shorter delivery times (category A for all sizes)
New design combining advantages of K2 and K4 adapters. |  | Very short and yet robust and rugged design
Adapter concept with coupling |  | Easy and fast motor assembly and disassembly for fast and efficient motor replacement
Flexible backlash free elastomer coupling |  | Long adapter service life due to absorption of shock loads & vibrations as well as compensation of slight shaft displacements
Variable bearing and sealing options |  | The right adapter for every application
4 different gear types (helical, parallel, bevel and helical-worm gear units) |  | The right gearbox-adapter combination for every application
NEW!

## Slide 5: Innomotics SG Geared Motors New IEC Motor Adapter Generation KU
Gearbox |  |  |  |  |  | KU Adapter |  |  |  |  |  |  |  |  |  |  |  |  |  |  | KU Adapter |  |  |  |  |  |  |  |  |  |  | 
E | Z | FZ | B | K | C | 63 | 71 | 80 | 90 | 100 | 112 | 132 | 160 | 180 | 200 | 225 | 250 |  | D | FD | 63 | 71 | 80 | 90 | 100 | 112 | 132 | 160 | 180 | 200 | 225 | 250
 | 19 |  | 19 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 19 |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 29 | 29 | 29 |  | 29 | ● | ● | ● | ● |  |  |  |  |  |  |  |  |  | 29 | 29 | ● | ● | ● | ● |  |  |  |  |  |  |  | 
39 | 39 | 39 | 39 | 39 | 39 | ● | ● | ● | ● | ● |  |  |  |  |  |  |  |  | 39 | 39 | ● | ● | ● | ● | ● |  |  |  |  |  |  | 
49 | 49 | 49 | 49 | 49 | 49 | ● | ● | ● | ● | ● | ● | ● |  |  |  |  |  |  | 49 | 49 | ● | ● | ● | ● | ● | ● | ● |  |  |  |  | 
 | 59 |  |  |  |  | ● | ● | ● | ● | ● | ● | ● |  |  |  |  |  |  | 59 |  | ● | ● | ● | ● | ● | ● | ● |  |  |  |  | 
 | 69 | 69 |  | 69 | 69 | ● | ● | ● | ● | ● | ● | ● |  |  |  |  |  |  | 69 | 69 | ● | ● | ● | ● | ● | ● | ● |  |  |  |  | 
 |  |  |  | 79 |  | ● | ● | ● | ● | ● | ● | ● |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
69 | 79 | 79 |  | 89 | 89 |  | ● | ● | ● | ● | ● | ● | ● |  |  |  |  |  | 79 | 79 |  | ● | ● | ● | ● | ● | ● | ● |  |  |  | 
89 | 89 | 89 |  | 109 |  |  |  | ● | ● | ● | ● | ● | ● | ● |  |  |  |  | 89 | 89 |  |  | ● | ● | ● | ● | ● | ● |  |  |  | 
109 | 109 | 109 |  | 129 |  |  |  |  | ● | ● | ● | ● | ● | ● | ● | ● |  |  | 109 | 109 |  |  |  | ● | ● | ● | ● | ● |  |  |  | 
129 | 129 | 129 |  | 149 |  |  |  |  | ● | ● | ● | ● | ● | ● | ● | ● | ● |  | 129 | 129 |  |  |  | ● | ● | ● | ● | ● |  |  |  | 
149 | 149 | 149 |  | 169 |  |  |  |  |  | ● | ● | ● | ● | ● | ● | ● | ● |  | 149 | 149 |  |  |  |  | ● | ● | ● | ● | ● | ● | ● | ●
 | 169 | 169 |  |  |  |  |  |  |  |  | ● | ● | ● | ● | ● | ● | ● |  | 169 | 169 |  |  |  |  |  | ● | ● | ● | ● | ● | ● | ●
 | 189 | 189 |  | 189 |  |  |  |  |  |  | ● | ● | ● | ● | ● | ● | ● |  | 189 | 189 |  |  |  |  |  | ● | ● | ● | ● | ● | ● | ●
Available Gearbox-Adapter Combinations
available
NEW!

## Slide 6: Innomotics SG Geared Motors New IEC Motor Adapter Generation KU
Adapter Bearing | KU Adapter |  |  |  |  |  |  |  |  |  |  | 
 | 63 | 71 | 80 | 90 | 100 | 112 | 132 | 160 | 180 | 200 | 225 | 250
Standard bearing | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ●
A30 reinforced bearing | ○ | ○ | ○ | ○ | ● | ● | ● | ● | ● | ● | ● | ●
Available Options
Adapter Sealing | KU Adapter |  |  |  |  |  |  |  |  |  |  | 
 | 63 | 71 | 80 | 90 | 100 | 112 | 132 | 160 | 180 | 200 | 225 | 250
Standard sealing | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ●
A35 FKM sealing | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ●
A36 Sealing long service life | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ● | ●
available
not available
NEW!

## Slide 7: Innomotics SG Geared Motors New IEC Motor Adapter Generation KU
FAQ’s | Answer
K2 adapter offers a slip clutch and backstop option. Are these options also available for KU adapter? | These options are not available for KU adapters. However, K2 adapter with slip clutch/backstop will stay in our portfolio.
KU shall replace K2 and K4 adapter but is only available up to size 250. K2 is available also in sizes 280 and 315? | These sizes are not available for KU adapters. However, K2 adapter 280 and 315 will stay in our portfolio.
Are the same gearbox-adapter combinations available for KU which were available for K2 and K4? | Yes.
Is the KU adapter available for NEMA motors? | No. Please use K3/K5 adapters.
Can KU adapters be used in explosive environments? | Yes.
Is the KU adapter available with fast track option (W50)? | Yes.